## Slide 1: CSE/PC/B/T/316 Computer Networks Topic 15- Network Layer Delivery, Forwarding and Routing
Sarbani Roy
sarbani.roy@jadavpuruniversity.in
Office: CC-5-7
Cell: 9051639328

## Slide 2
DELIVERY
The network layer supervises the handling of the packets by the underlying physical networks. We define this handling as the delivery of a packet.
Direct Versus Indirect Delivery
Topics discussed in this section:

## Slide 3
Direct and indirect delivery

## Slide 4
FORWARDING
Forwarding means to place the packet in its route to its destination. Forwarding requires a host or a router to have a routing table. When a host has a packet to send or when a router has received a packet to be forwarded, it looks at this table to find the route to the final destination.
Forwarding Techniques Forwarding Process
Routing Table
Topics discussed in this section:

## Slide 5
Route method versus next-hop method

## Slide 6
Host-specific versus network-specific method

## Slide 7
Default method

## Slide 8
Simplified forwarding module in classless address

## Slide 9
In classless addressing, we need at least four columns in a routing table.
Note

## Slide 10
Make a routing table for router R1, using the configuration in Figure below.
Example

## Slide 11
Show the forwarding process if a packet arrives at R1 with the destination address 180.70.65.140.
Example
Solution
The router performs the following steps:
1. The first mask (/26) is applied to the destination address. The result is 180.70.65.128, which does not match the corresponding network address.
2. The second mask (/25) is applied to the destination address. The result is 180.70.65.128, which matches the corresponding network address. The next-hop address and the interface number m0 are passed to ARP for further processing.

## Slide 12
Show the forwarding process if a packet arrives at R1 with the destination address 201.4.22.35.
Example
Solution
The router performs the following steps:
1. The first mask (/26) is applied to the destination address. The result is 201.4.22.0, which does not match the corresponding network address.
2. The second mask (/25) is applied to the destination address. The result is 201.4.22.0, which does not match the corresponding network address (row 2).

## Slide 13
Example (continued)
3. The third mask (/24) is applied to the destination address. The result is 201.4.22.0, which matches the corresponding network address. The destination address of the packet and the interface number m3 are passed to ARP.

## Slide 14
Show the forwarding process if a packet arrives at R1 with the destination address 18.24.32.78.
Example
Solution
This time all masks are applied, one by one, to the destination address, but no matching network address is found. When it reaches the end of the table, the module gives the next-hop address 180.70.65.200 and interface number m2 to ARP. This is probably an outgoing package that needs to be sent, via the default router, to someplace else in the Internet.

## Slide 15
Address aggregation

## Slide 16
Longest mask matching

## Slide 17
As an example of hierarchical routing, let us consider Figure next. A regional ISP is granted 16,384 addresses starting from 120.14.64.0. The regional ISP has decided to divide this block into four subblocks, each with 4096 addresses. Three of these subblocks are assigned to three
local ISPs; the second subblock is reserved for future use. Note that the mask for each block is /20 because the original block with mask /18 is divided into 4 blocks.
Example
The first local ISP has divided its assigned subblock into 8 smaller blocks and assigned each to a small ISP. Each small ISP provides services to 128 households, each using four addresses.

## Slide 18
The second local ISP has divided its block into 4 blocks and has assigned the addresses to four large organizations.
Example (continued)
There is a sense of hierarchy in this configuration. All routers in the Internet send a packet with destination address 120.14.64.0 to 120.14.127.255 to the regional ISP.
The third local ISP has divided its block into 16 blocks and assigned each block to a small organization. Each small organization has 256 addresses, and the mask is /24.

## Slide 19
Hierarchical routing with ISPs

## Slide 20
Common fields in a routing table

## Slide 21
One utility that can be used to find the contents of a routing table for a host or router is netstat in UNIX or LINUX. The next slide shows the list of the contents of a default server. We have used two options, r and n. The option r indicates that we are interested in the routing table, and the option n indicates that we are looking for numeric addresses. Note that this is a routing table for a host, not a router. Although we discussed the routing table for a router throughout the chapter, a host also needs a routing table.
Example

## Slide 22
Example (continued)
The destination column here defines the network address. The term gateway used by UNIX is synonymous with router. This column actually defines the address of the next hop. The value 0.0.0.0 shows that the delivery is direct. The last entry has a flag of G, which means that the destination can be reached through a router (default router). The Iface defines the interface.

## Slide 23
Example (continued)
More information about the IP address and physical address of the server can be found by using the ifconfig command on the given interface (eth0).

## Slide 24
Figure Configuration of the server

## Slide 25
UNICAST ROUTING PROTOCOLS
A routing table can be either static or dynamic. A static table is one with manual entries. A dynamic table is one that is updated automatically when there is a change somewhere in the Internet. A routing protocol is a combination of rules and procedures that lets routers in the Internet inform each other of changes.
Optimization Intra- and Interdomain Routing
Distance Vector Routing and RIP
Link State Routing and OSPF
Path Vector Routing and BGP
Topics discussed in this section:

## Slide 26
Autonomous systems

## Slide 27
Popular routing protocols

## Slide 28
Distance vector routing tables

## Slide 29
Initialization of tables in distance vector routing

## Slide 30
In distance vector routing, each node shares its routing table with its
immediate neighbors periodically and when there is a change.
Note

## Slide 31
Updating in distance vector routing

## Slide 32
Two-node instability

## Slide 33
Three-node instability

## Slide 34
Example of a domain using RIP

## Slide 35
Concept of link state routing

## Slide 36
Link state knowledge

## Slide 37
Dijkstra algorithm

## Slide 38
Example of formation of shortest path tree

## Slide 39
Routing table for node A

## Slide 40
Areas in an autonomous system

## Slide 41
Types of links

## Slide 42
Point-to-point link

## Slide 43
Transient link

## Slide 44
Stub link

## Slide 45
Example of an AS and its graphical representation in OSPF

## Slide 46
Initial routing tables in path vector routing

## Slide 47
Stabilized tables for three autonomous systems

## Slide 48
Internal and external BGP sessions

## Slide 49
MULTICAST ROUTING PROTOCOLS
In this section, we discuss multicasting and multicast routing protocols.
Unicast, Multicast, and Broadcast Applications
Multicast Routing
Routing Protocols
Topics discussed in this section:

## Slide 50
Unicasting

## Slide 51
In unicasting, the router forwards the received packet through
only one of its interfaces.
Note

## Slide 52
Multicasting

## Slide 53
In multicasting, the router may forward the received packet
through several of its interfaces.
Note

## Slide 54
Multicasting versus multiple unicasting

## Slide 55
Emulation of multicasting through multiple unicasting is not efficient
and may create long delays, particularly with a large group.
Note

## Slide 56
In unicast routing, each router in the domain has a table that defines
a shortest path tree to possible destinations.
Note

## Slide 57
Shortest path tree in unicast routing

## Slide 58
In multicast routing, each involved router needs to construct
a shortest path tree for each group.
Note

## Slide 59
Source-based tree approach

## Slide 60
In the source-based tree approach, each router needs to have one shortest path tree for each group.
Note

## Slide 61
Group-shared tree approach

## Slide 62
In the group-shared tree approach, only the core router, which has a shortest path tree for each group, is involved in multicasting.
Note

## Slide 63
Taxonomy of common multicast protocols

## Slide 64
Multicast link state routing uses the source-based tree approach.
Note

## Slide 65
Flooding broadcasts packets, but creates loops in the systems.
Note

## Slide 66
RPF eliminates the loop in the flooding process.
Note

## Slide 67
Reverse path forwarding (RPF)

## Slide 68
Problem with RPF

## Slide 69
RPF Versus RPB

## Slide 70
RPB creates a shortest path broadcast tree from the source to each destination.
It guarantees that each destination receives one and only one copy of the packet.
Note

## Slide 71
RPF, RPB, and RPM

## Slide 72
RPM adds pruning and grafting to RPB to create a multicast shortest
path tree that supports dynamic membership changes.
Note

## Slide 73
Group-shared tree with rendezvous router

## Slide 74
Sending a multicast packet to the rendezvous router

## Slide 75
In CBT, the source sends the multicast packet (encapsulated in a unicast packet) to the core router. The core router decapsulates the packet and forwards it to all interested interfaces.
Note

## Slide 76
PIM-DM is used in a dense multicast environment, such as a LAN.
Note

## Slide 77
PIM-DM uses RPF and pruning and grafting strategies to handle multicasting.
However, it is independent of the underlying unicast protocol.
Note

## Slide 78
PIM-SM is used in a sparse multicast environment such as a WAN.
Note

## Slide 79
PIM-SM is similar to CBT but uses a simpler procedure.
Note

## Slide 80
Logical tunneling

## Slide 81
MBONE