## Slide 1: CSE/PC/B/T/316 Computer Networks Topic 17- Transport Layer Process-to-Process Delivery: TCP
Sarbani Roy
sarbani.roy@jadavpuruniversity.in
Office: CC-5-7
Cell: 9051639328

## Slide 2
TCP
TCP is a connection-oriented protocol; it creates a virtual connection between two TCPs to send data. In addition, TCP uses flow and error control mechanisms at the transport level.
TCP Services TCP Features
Segment
A TCP Connection
Flow Control
Error Control
Topics discussed in this section:

## Slide 3
Table Well-known ports used by TCP

## Slide 4
Figure Stream delivery

## Slide 5
Figure Sending and receiving buffers

## Slide 6
Figure TCP segments

## Slide 7
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with a randomly generated number.
Note

## Slide 8
The following shows the sequence number for each segment:
Example

## Slide 9
The value in the sequence number field of a segment defines the
number of the first data byte contained in that segment.
Note

## Slide 10
The value of the acknowledgment field in a segment defines
the number of the next byte a party expects to receive.
The acknowledgment number is cumulative.
Note

## Slide 11
Figure TCP segment format

## Slide 12
Figure Control field

## Slide 13
Table Description of flags in the control field

## Slide 14
Figure Connection establishment using three-way handshaking

## Slide 15
A SYN segment cannot carry data, but it consumes one sequence number.
Note

## Slide 16
A SYN + ACK segment cannot carry data, but does consume one sequence number.
Note

## Slide 17
An ACK segment, if carrying no data, consumes no sequence number.
Note

## Slide 18
Figure Data transfer

## Slide 19
Figure Connection termination using three-way handshaking

## Slide 20
The FIN segment consumes one sequence number if it does not carry data.
Note

## Slide 21
The FIN + ACK segment consumes one sequence number if it does not carry data.
Note

## Slide 22
Figure Half-close

## Slide 23: Flow Control
Sliding Window Protocol

## Slide 24
Figure Sliding window

## Slide 25
A sliding window is used to make transmission more efficient as well as
to control the flow of data so that the destination does not become
overwhelmed with data. TCP sliding windows are byte-oriented.
Note

## Slide 26
What is the value of the receiver window (rwnd) for host A if the receiver, host B, has a buffer size of 5000 bytes and 1000 bytes of received and unprocessed data?
Example
Solution
The value of rwnd = 5000 − 1000 = 4000. Host B can receive only 4000 bytes of data before overflowing its buffer. Host B advertises this value in its next segment to A.

## Slide 27
What is the size of the window for host A if the value of rwnd is 3000 bytes and the value of cwnd is 3500 bytes?
Example
Solution
The size of the window is the smaller of rwnd and cwnd, which is 3000 bytes.

## Slide 28
Figure shows an unrealistic example of a sliding window. The sender has sent bytes up to 202. We assume that cwnd is 20 (in reality this value is thousands of bytes). The receiver has sent an acknowledgment number of 200 with an rwnd of 9 bytes (in reality this value is thousands of bytes). The size of the sender window is the minimum of rwnd and cwnd, or 9 bytes. Bytes 200 to 202 are sent, but not acknowledged. Bytes 203 to 208 can be sent without worrying about acknowledgment. Bytes 209 and above cannot be sent.
Example

## Slide 29
Some points about TCP sliding windows:
❏ The size of the window is the lesser of rwnd and cwnd.
❏ The source does not have to send a full window’s worth of data.
❏ The window can be opened or closed by the receiver, but should not be shrunk.
❏ The destination can send an acknowledgment at any time as long as it does not result in a shrinking window.
❏ The receiver can temporarily shut down the window; the sender, however, can always send a segment of 1 byte after the window is shut down.
Note

## Slide 30: Error Control
Checksum
Acknowledgement
Retransmission
Retransmission after RTO
Retransmission after three duplicate ACK Segments
Out of order Segments
Lost segment
Fast retransmission

## Slide 31
ACK segments do not consume sequence numbers and are not acknowledged.
Note

## Slide 32
In modern implementations, a retransmission occurs if the retransmission timer expires or three duplicate ACK segments have arrived.
Note

## Slide 33
No retransmission timer is set for an ACK segment.
Note

## Slide 34
Data may arrive out of order and be temporarily stored by the receiving TCP,
but TCP guarantees that no out-of-order segment is delivered to the process.
Note

## Slide 35
Figure Normal operation

## Slide 36
Figure Lost segment

## Slide 37
The receiver TCP delivers only ordered data to the process.
Note

## Slide 38
Figure Fast retransmission

## Slide 39: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  unreliable datagram
  reliable, byte stream-oriented
a host-local, application-created/owned,
OS-controlled interface (a “door”) into which
application process can both send and
receive messages to/from another (remote or
local) application process
socket
Goal: learn how to build client/server applications that communicate using sockets

## Slide 40: Socket-programming using TCP
Socket: a door between application process and end-end-transport protocol (UDP or TCP)
TCP service: reliable transfer of bytes from one process to another
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet
The application developer has the ability to fix a few TCP parameters, such as maximum buffer and maximum segment sizes.

## Slide 41: Sockets for server and client
Server
  Welcoming socket
    Welcomes some initial contact from a client.
  Connection socket
    Is created at initial contact of client.
    New socket that is dedicated to the particular client.
Client
  Client socket
    Initiate a TCP connection to the server by creating a socket object. (Three-way handshake)
    Specify the address of the server process, namely, the IP address of the server and the port number of the process.

## Slide 42: Sockets
Client socket, welcoming socket and connection socket

## Slide 43: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  allows server to talk with multiple clients
TCP provides reliable, in-order
transfer of bytes (“pipe”)
between client and server
application viewpoint

## Slide 44: Socket functional calls
socket (): Create a socket
bind(): bind a socket to a local IP address and port #
listen(): passively waiting for connections
connect(): initiating connection to another socket
accept(): accept a new connection
Write(): write data to a socket
Read(): read data from a socket
sendto(): send a datagram to another UDP socket
recvfrom(): read a datagram from a UDP socket
close(): close a socket (tear down the connection)

## Slide 45
TCP
IP
Ethernet Adapter
Web Server
Port 80
For example: web server
What does a web server need to do so that a web client can connect to it?
TCP Server

## Slide 46: TCP Client
TCP
IP
Ethernet Adapter
2 Web Clients
For example: web client
How does a web client connect to a web server?

## Slide 47
Since web traffic uses TCP, the web server must create a socket of type SOCK_STREAM
int fd; /* socket descriptor */
if((fd = socket(AF_INET, SOCK_STREAM, 0)) < 0) {
perror(“socket”);
exit(1);
}
socket returns an integer (socket descriptor)
  fd < 0 indicates that an error occurred
AF_INET associates a socket with the Internet protocol family
SOCK_STREAM selects the TCP protocol
Socket I/O: socket()

## Slide 48
A socket can be bound to a port
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
/* create the socket */
srv.sin_family = AF_INET; /* use the Internet addr family */
srv.sin_port = htons(80); /* bind socket ‘fd’ to port 80*/
/* bind: a client may connect to any of my addresses */
srv.sin_addr.s_addr = htonl(INADDR_ANY);
if(bind(fd, (struct sockaddr*) &srv, sizeof(srv)) < 0) {
perror("bind"); exit(1);
}
Still not quite ready to communicate with a client...
Socket I/O: bind()

## Slide 49: Socket I/O: listen()
listen indicates that the server will accept a connection
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
/* 1) create the socket */
/* 2) bind the socket to a port */
if(listen(fd, 5) < 0) {
perror(“listen”);
exit(1);
}
Still not quite ready to communicate with a client...

## Slide 50: Socket I/O: accept()
accept blocks waiting for a connection
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by bind() */
struct sockaddr_in cli; /* used by accept() */
int newfd; /* returned by accept() */
int cli_len = sizeof(cli); /* used by accept() */
/* 1) create the socket */
/* 2) bind the socket to a port */
/* 3) listen on the socket */
newfd = accept(fd, (struct sockaddr*) &cli, &cli_len);
if(newfd < 0) {
perror("accept"); exit(1);
}
accept returns a new socket (newfd) with the same properties as the original socket (fd)
  newfd < 0 indicates that an error occurred

## Slide 51: Socket I/O: accept() continued...
struct sockaddr_in cli; /* used by accept() */
int newfd; /* returned by accept() */
int cli_len = sizeof(cli); /* used by accept() */
newfd = accept(fd, (struct sockaddr*) &cli, &cli_len);
if(newfd < 0) {
perror("accept");
exit(1);
}
How does the server know which client it is?
  cli.sin_addr.s_addr contains the client’s IP address
  cli.sin_port contains the client’s port number
Now the server can exchange data with the client by using read and write on the descriptor newfd.
Why does accept need to return a new descriptor?

## Slide 52: Socket I/O: read()
read can be used with a socket
read blocks waiting for data from the client but does not guarantee that sizeof(buf) is read
int fd; /* socket descriptor */
char buf[512]; /* used by read() */
int nbytes; /* used by read() */
/* 1) create the socket */
/* 2) bind the socket to a port */
/* 3) listen on the socket */
/* 4) accept the incoming connection */
if((nbytes = read(newfd, buf, sizeof(buf))) < 0) {
perror(“read”); exit(1);
}

## Slide 53: Dealing with IP Addresses
struct sockaddr_in srv;
srv.sin_addr.s_addr = inet_addr(“128.2.35.50”);
if(srv.sin_addr.s_addr == (in_addr_t) -1) {
fprintf(stderr, "inet_addr failed!\n"); exit(1);
}
Converting a numerical address to a string:
IP Addresses are commonly written as strings (“128.2.35.50”), but programs deal with IP addresses as integers.
struct sockaddr_in srv;
char *t = inet_ntoa(srv.sin_addr);
if(t == 0) {
fprintf(stderr, “inet_ntoa failed!\n”); exit(1);
}
Converting strings to numerical address:

## Slide 54: Translating Names to Addresses
gethostbyname provides interface to DNS
Additional useful calls
  gethostbyaddr – returns hostent given sockaddr_in
  getservbyname
    Used to get service description (typically port number)
    Returns servent based on name
#include <netdb.h>
struct hostent *hp; /*ptr to host info for remote*/
struct sockaddr_in peeraddr;
char *name = “www.cs.cmu.edu”;
peeraddr.sin_family = AF_INET;
hp = gethostbyname(name)
peeraddr.sin_addr.s_addr = ((struct in_addr*)(hp->h_addr))->s_addr;

## Slide 55: Socket I/O: connect()
connect allows a client to connect to a server...
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by connect() */
/* create the socket */
/* connect: use the Internet address family */
srv.sin_family = AF_INET;
/* connect: socket ‘fd’ to port 80 */
srv.sin_port = htons(80);
/* connect: connect to IP Address “128.2.35.50” */
srv.sin_addr.s_addr = inet_addr(“128.2.35.50”);
if(connect(fd, (struct sockaddr*) &srv, sizeof(srv)) < 0) {
perror(”connect"); exit(1);
}

## Slide 56: Socket I/O: write()
write can be used with a socket
int fd; /* socket descriptor */
struct sockaddr_in srv; /* used by connect() */
char buf[512]; /* used by write() */
int nbytes; /* used by write() */
/* 1) create the socket */
/* 2) connect() to the server */
/* Example: A client could “write” a request to a server */
if((nbytes = write(fd, buf, sizeof(buf))) < 0) {
perror(“write”);
exit(1);
}

## Slide 57: Review: TCP Client-Server Interaction
socket()
bind()
listen()
accept()
write()
read()
read()
TCP Server
close()
socket()
TCP Client
connect()
write()
read()
close()
connection establishment
data request
data reply
end-of-file notification
from UNIX Network Programming Volume 1, figure 4.1