## Slide 1: CSE/PC/B/T/316 Computer Networks Topic 9- IEEE 802.15.1 Bluetooth
Sarbani Roy
sarbani.roy@jadavpuruniversity.in
Office: CC-5-7
Cell: 9051639328

## Slide 2: Bluetooth
Bluetooth is a wireless LAN technology 802.15 (Wireless Personal Area Network) designed to connect devices of different functions such as telephones, notebooks, computers, cameras, printers, coffee makers, and so on. A Bluetooth LAN is an ad hoc network, which means that the network is formed spontaneously.

## Slide 3: Bluetooth Overview
Wireless technology for short-range voice and data communication
  Devices can communicate with each other with wireless connectivity
Low-cost and low-power
Connects a wide range of computing and telecommunication devices
Expand communication capabilities
Provides a communication platform between a wide range of “smart” devices
Not limited to “line of sight” communication

## Slide 4: Summary
Bluetooth is a global, RF-based (ISM band: 2.4 GHz), short-range, connectivity solution for portable, personal devices
  it is not just a radio, it is an end-to-end solution
The Bluetooth spec comprises
  a HW & SW protocol specification
  usage case scenario profiles and interoperability requirements
IEEE 802.15.1 is working on standardizing the PHY and MAC layers in Bluetooth
More Info:
  http://www.bluetooth.org
  http://ieee802.org/15/pub/TG1.html

## Slide 5: Products
Notebook PCs & desktop computers
Printers
PDAs
Other handheld devices
Cell phones
Wireless periperals:
  Headsets
  Cameras
Access Points
CD Player
TV/VCR/DVD
Telephone Answering Devices
Cordless Phones
Cars
Hands free calls

## Slide 6: Connecting to Internet
Being able to gain access to the Internet by using “Bluetooth access points”
  Access point is used as a gateway to the internet
  Both the access point and the device are Bluetooth-enabled
  An example of Service Discovery Protocol
    Access point provides a service to the device

## Slide 7: Bluetooth Specifications
Things that you must have:
  Transceivers and Receivers that can send and receive data because they use Radio Waves.
  MAC Address (Physical Address)
    Burnt on the NIC card by the manufacturer.
  PIN Number
    To identify the user using the device.
  A Piconet
  A FHSS protocol

## Slide 8: The Bluetooth network topology
M
M
S
S
S
S
P
sb
sb
P
P
Radio designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to 7 simultaneous or 200+ inactive (parked) slaves per piconet
  Each piconet has maximum capacity (1 MSPS (Mega Samples Per Second)
  Unique hopping pattern/ID
Scatternet
  Piconets can coexist in time and space

## Slide 9
Piconet

## Slide 10
Scatternet

## Slide 11: Establishing Piconets
Whenever there is a connection between two Bluetooth devices, a piconet is formed
Always 1 master and up to 7 active slaves
Any Bluetooth device can be either a master or a slave
Can be a master of one piconet and a slave of another piconet at the same time (scatternet)
All devices have the same timing and frequency hopping sequence

## Slide 12: Scatternets
Formed by two or more Piconets
Master of one piconet can participate as a slave in another connected piconet
No time or frequency synchronization between piconets

## Slide 13: The Piconet
or
A
D
C
B
E
All devices in a piconet hop together
  To form a piconet: master gives slaves its clock and device ID
    Hopping pattern determined by device ID (48-bit)
    Phase in hopping pattern determined by Clock
Non-piconet devices are in standby
Piconet Addressing
  Active Member Address (AMA, 3-bits)
  Parked Member Address (PMA, 8-bits)

## Slide 14: Inter-connected Piconets - The Scatternet
Complex
slave
master
master/slave
Printer
Laptop
Laptop
Mouse
Mobile Phone
Headset
LAN
Access Point

## Slide 15: FHSS
Bluetooth devices use a protocol called (FHSS) Frequency-Hopping Spread Spectrum .
Uses packet-switching to send data.
Bluetooth sends packets of data on a range of frequencies.
In each session one device is a master and the others are slaves.
The master device decides at which frequency data will travel.

## Slide 16: FHSS
Transceivers “hop” among 79 different frequencies in the 2.4 GHz baud at a rate of 1600 frequency hops per second.
The master device tells the slaves at what frequency data will be sent.
This technique allows devices to communicate with each other more securely.

## Slide 17: FHHS Example
Source: http://www.xircom.com

## Slide 18: The Bluetooth protocols
Application Framework and Support
Link Manager and L2CAP
Radio & Baseband
Host Controller Interface
RF
Baseband
Audio
Link Manager
L2CAP
Other
TCS
RFCOMM
Data
A hardware/software description
An application framework
SDP
Applications
Control

## Slide 19: Core Protocols
Radio: Specification of the air interface, i.e., frequencies, modulation, and transmit power
Baseband: Description of basic connection establishment, packet formats, timing, and basic QoS parameters
Link manager protocol: Link set-up and management between devices including security functions and parameter negotiation
Logical link control and adaptation protocol (L2CAP): Adaptation of higher layers to the baseband (connectionless and connection-oriented services
Service discovery protocol: Device discovery in close proximity plus querying of service characteristics

## Slide 20
Single-secondary communication

## Slide 21
Multiple-secondary communication

## Slide 22
Frame format types

## Slide 23: Access code
The access code consists of a 4 bit preamble, a synchronization field, and a trailer (if a packet header follows).
The 64-bit synchronization field is derived from the lower 24 bit of an address (lower address part, LAP).
  If the access code is used for channel access (i.e., data transmission between a master and a slave or vice versa), the LAP is derived from the master’s globally unique 48-bit address.
  In case of paging the LAP of the paged device is used.
  If a Bluetooth device wants to discover other (arbitrary) devices in transmission range (general inquiry procedure) it uses a special reserved LAP.
Special LAPs can be defined for inquiries of dedicated groups of devices.

## Slide 24: Packet header: address, type
This field contains typical layer 2 features: address, packet type, flow and error control, and checksum.
The 3-bit active member address represents the active address of a slave Active addresses are temporarily assigned to a slave in a piconet.
  If a master sends data to a slave the address is interpreted as receiver address.
  If a slave sends data to the master the address represents the sender address.
  The zero value is reserved for a broadcast from the master to all slaves.
The 4-bit type field determines the type of the packet.

## Slide 25: Packet header: flow, ARQN
A simple flow control mechanism for asynchronous traffic uses the 1-bit flow field.
  If a packet is received with flow=0 asynchronous data, transmission must stop.
  As soon as a packet with flow=1 is received, transmission may resume.
If an acknowledgement of packets is required, Bluetooth sends this in the slot following the data (using its time division duplex scheme).

## Slide 26: Packet header: SEQN, HEC
A simple alternating bit protocol with a single bit sequence number SEQN and acknowledgement number ARQN can be used.
An 8-bit header error check (HEC) is used to protect the packet header.
The packet header is also protected by a one-third rate forward error correction (FEC) code because it contains valuable link information and should survive bit errors. Therefore, the 18-bit header requires 54 bits in the packet.

## Slide 27
L2CAP data packet format

## Slide 28: Baseband Layer
Provides in-order delivery of byte streams
Handles Frequency Hop Sequences for Synchronization and Transmission
Establishes Links
  Synchronous Connection Oriented (SCO)
  Asynchronous Connection-Less (ACL)
Provides functionality to determine nearby Bluetooth devices

## Slide 29: SCO
Classical telephone (voice) connections require symmetrical, circuit-switched, point-to-point connections.
For this type of link, the master reserves two consecutive slots (forward and return slots) at fixed intervals.
  A master can support up to three simultaneous SCO links to the same slave or to different slaves.
  A slave supports up to two links from different masters or up to three links from the same master.
Using an SCO link, three different types of single-slot packets can be used

## Slide 30: ACL
Typical data applications require symmetrical or asymmetrical (e.g., web traffic), packet-switched, point-to-multipoint transfer scenarios (including broadcast).
Here the master uses a polling scheme. A slave may only answer if it has been addressed in the preceding slot.
Only one ACL link can exist between a master and a slave.
For ACLs carrying data, 1-slot, 3-slot or 5-slot packets can be used

## Slide 31: Example data transmission
The master always uses the even frequency slots, the odd slots are for the slaves.
In this example every sixth slot is used for an SCO link between the master and slave 1. The ACL links use single or multiple slots providing asymmetric bandwidth for connectionless packet transmission. This example again shows the hopping sequence which is independent of the transmission of packets.

## Slide 32: Functional Overview
Standby
  Waiting to join a piconet
Inquire
  Ask about radios to connect to
Page
  Connect to a specific radio
Connected
  Actively on a piconet (master or slave)
Park/Hold
  Low Power connected states

## Slide 33: Link Manager Operation
Devices operate in standby mode by default until they become connected to a piconet
4 Connection Modes
  Active
  Hold
  Park
  Sniff
Modes allow devices to adjust power consumption, performance, and the number/role of participants in a piconet

## Slide 34: Active Mode
Limited to 7 Active slaves for each master
Three bit address (AM_ADDR) given to each active slave
Unit actively participates on channel
Can receive communications in any given frame
Active slaves are polled by master for transmissions
Unit operates on high-power

## Slide 35: Hold Mode
Frees slave to
  Attend another Piconet
  Perform scanning, paging, or inquiry operations
  Move into low-power sleep
Unit keeps active member address
Unit does not support ACL packets on the channel but may support SCO packets
Master and slave agree on a one time hold duration after which the slave revives and synchronizes with channel traffic
Unit operates on low-power

## Slide 36: Sniff Mode
Very similar to hold mode
Slave is freed for reoccurring fixed time intervals
Master can only communicate during arranged “sniff” time slots

## Slide 37: Park Mode
Parked unit gives up active member address and is assigned
  8 bit Parked member address (PM_ADDR) – allows master to unpark slave
  8 bit Access request address (AR_ADDR) – allows slave to ask master to unpark it
Unit stays synchronized to channel
Operates in very low-power sleep

## Slide 38: Park Mode (cont.)
Provides the ability to connect more than 7 devices to a master (8 bit PM_ADDR allows 255 parked devices)
Active and Parked slaves can be switched in and out to allow many connections to a single piconet

## Slide 39: Bluetooth Security
There are three modes of security for Bluetooth access between two devices.
  non-secure
  service level enforced security
  link level enforced security
Device security level
  Trusted
  untrusted
Service security level
  Authorization and Authentication
  Authentication only
  Open to all devices

## Slide 40: Bluetooth Security
The following are the three basic security services specified in the Bluetooth standard:
  Authentication
    verifying the identity of communicating devices. User authentication is not provided natively by Bluetooth.
  Confidentiality
    preventing information compromise caused by eavesdropping by ensuring that only authorized devices can access and view data.
  Authorization
    allowing the control of resources by ensuring that a device is authorized to use a service before permitting it to do so.

## Slide 41: Security
Authentication and encryption is provided at the Link Manager layer.
The PIN is translated into a 128 bit link key which is used for authentication.
After authentication the radios will settle on a suitable length encryption key to be used.
Bluetooth relies on PIN codes to establish trusted relationships between devices.